## Slide 1
Final Year Project On,
MIMO Antenna in
5G Communication
Presented by:
Nabanita Saha (T91/ECE/184047)
Tamojit Das (T91/ECE/184052)
Under supervision of:
Dr. Kaushik Mandal (Assistant. Professor, RPE, CU)
Institute of Radiophysics and Electronics
University of Calcutta
June 2022

## Slide 3
Outline
What is MIMO technology?
Literature Review
Design evolution and corresponding antenna performance
Parametric Studies
Radiation Pattern, ECC, DG
Motivation and Objective
Proposed MIMO antenna
Fabricated Prototype and
Measured Results

## Slide 4
Increased demand of 5G usage
MIMO antenna is the obvious choice for the 5G applications
Mutual coupling among the antenna elements is the key factor for a MIMO antenna
Enough scope is there to work with the placement of antenna elements for better isolation
Motivation
Design and analysis of MIMO antenna for 5G applications
Sub 6 GHz band is the target operating band
Improvement of isolation between the antenna elements
Design that can provide both space and pattern diversity
Objective

## Slide 5
What is MIMO Technology ?
MIMO (multiple input, multiple output) is an antenna technology for wireless communications in which multiple antennas are used at both the source (transmitter) and the destination (receiver).

## Slide 6
Proposed
MIMO Antenna
With Better Isolation

## Slide 7
Frequency /GHz
dB
S-parameter (S11)
Front View
Back View
Design 1: Single Monopole
Design Parameters:
Antenna Patch
Length = 21.484023919693 mm,
Width = 27.922505310634 mm,
Height = 0.035 mm
Feed Line
Length = 14.5 mm,
Width = 5.5845010621268 mm,
Height = 0.035 mm
Materials Details:
Dielectric Material – FR4
Patch and Ground – Copper
Operating band: 2.1087 – 4.4534 GHz
Band Width : 2.3447 GHz
* (Design Parameters and Materials Details are same for all 4 designs)

## Slide 8
S-parameters
Front View
Back View
Design 2: Orthogonal placement of Two Monopoles
Operating Band: 3.2505 – 4.6002 GHz
Band Width: 1.3497 GHz
Maximum S21: -13 dB

## Slide 9
S-parameters
Front View
Back View
Design 3: Two Monopoles orthogonally opposite side of the Substrate
Operating Band: 3.2396 – 4.5971 GHz
Band Width: 1.3575 GHz
Maximum S21: -13.5 dB

## Slide 10
S-parameters
Front View
Back View
Design 4: Two Monopoles opposite along X axis
Operating Band: 2.0838 – 4.1218 GHz
Band Width: 2.038 GHz
Maximum S21: -16 dB

## Slide 11
Design Modification
Design: A
Design: B
Design: C
Final Proposed Design
Design Parameters:
Dielectric length =150 mm
Dielectric width =150 mm
Dielectric height =1.6 mm
Patch length =27.922505310634 mm
Patch width =21.484023919693 mm
Patch height =0.035mm
Feed length=14.5 mm
Feed width =5.5845010621268 mm
Cut width=2 mm
Operating Band – (1.4556 – 4.5015) GHz
Band Width – 3.0459 GHz
Percentage bandwidth – 102.2%
Indicator:

## Slide 12
Feed width = W/10
Parametric Studies (design A) : Feed Width Variation
Feed width = W/10
Feed width = W/7.5
Feed width = W/4
Feed width = W/5

## Slide 13
Parametric Studies (design A) : Ground Length Variation
Ground length = L/2
Ground length = L/1.5
Ground length = L
Ground length = L – 28

## Slide 14
Comparison of S Parameters for Respective Design Modifications
1)
2)
3)
4)
3)
Design A
Design B
Design C
Final Proposed Design

## Slide 15
Radiation
Pattern
Port 1
Port 2
Port 4
Port 3

## Slide 16
1.4
Envelope
Correlation
Coefficient
Diversity
Gain

## Slide 17
Fabricated Prototype and Measured Results
Fabricated Antenna
Comparison Between Simulated
and
Measured Results of
S-Parameters
Copper Patch
on Front Side
Copper Patch
on Rear Side
Ground
Cuts
SMA Connectors
1
2
3
4

## Slide 18
Thank
you!